## Slide 1
Infrared Optical Parametric Oscillator
Frequency Combs
  Prof. Derryck Reid
  Institute of Photonics and Quantum Sciences
  Heriot-Watt University
Notes: Heriot Watt has been active in frequency comb research since 2004. We have built a large number of modelocked Ti:sapphire lasers that provided fully-locked combs up to repetition frequencies of 500 MHz. Specifically, we developed a full comb on a single breadboard in 2011 (photo) as a demonstrator for M Squared Lasers, who subsequently licensed the technology from us. This is potentially important in as much as our contribution of comb technology to the ELT project could be supported by M Squared Lasers as potential manufacturing partner.
We have published a number of papers with NPL. In collaboration with Patrick Gill’s group we developed a robust new method for comb stabilisation, which provided a factor of 10 reduction in phase noise compared to the state of the art nonlinear interferometer. The figure below (left) shows graphically the noise improvement we achieved.
In the bottom right figure we show the radio frequency spectrum from our 500-MHz laser, and a zoomed in spectrum of the locked comb offset frequency of 10 MHz. Since 2004 we have increasingly developed more of our own locking electronics, so we have a large amount of control and flexibility in the locking circuits we use.

## Slide 2
Motivation – HIRES calibration requirements
Introduction to OPO frequency comb technology
  Concepts and operating principles
  Comb-offset control in a fs OPO
Comb stability characterisations
  250-MHz OPO comb
  333-MHz OPO comb
  Harmonically-pumped 1-GHz OPO comb
  Fundamentally-pumped 1-GHz OPO comb
Towards multi-GHz OPO combs
  FP-filtering to 10-GHz
  Progress towards 10-GHz OPO combs
Outline
Notes: Heriot Watt has been active in frequency comb research since 2004. We have built a large number of modelocked Ti:sapphire lasers that provided fully-locked combs up to repetition frequencies of 500 MHz. Specifically, we developed a full comb on a single breadboard in 2011 (photo) as a demonstrator for M Squared Lasers, who subsequently licensed the technology from us. This is potentially important in as much as our contribution of comb technology to the ELT project could be supported by M Squared Lasers as potential manufacturing partner.
We have published a number of papers with NPL. In collaboration with Patrick Gill’s group we developed a robust new method for comb stabilisation, which provided a factor of 10 reduction in phase noise compared to the state of the art nonlinear interferometer. The figure below (left) shows graphically the noise improvement we achieved.
In the bottom right figure we show the radio frequency spectrum from our 500-MHz laser, and a zoomed in spectrum of the locked comb offset frequency of 10 MHz. Since 2004 we have increasingly developed more of our own locking electronics, so we have a large amount of control and flexibility in the locking circuits we use.

## Slide 3
idler
signal
signal & idler SHG
pump, signal & idler SFM
ESPRESSO
E-ELT HIRES
0.5 1 1.5 2 2.5 3 3.5 4
OPO wavelength (µm)
Motivation – HIRES calibration requirements
Wavelength tuning capability of a Ti:sapphire-pumped OPO, compared with:
  ESPRESSO (Blue arm: 380 – 520 nm; Red arm: 520 – 780 nm)
  HIRES (0.37 μm to 2.5 μm)
This wavelength coverage is extremely challenging for laser frequency combs
   motivates development of suitable OPO combs
Notes: Core expertise in our group is the frequency conversion of modelocked lasers using optical parametric oscillators (“OPOs”) which allow a near-IR laser to be converted into the mid-IR, or (via frequency doubling) into tunable visible light. In 2007 our group was the first to extend the femtosecond frequency comb concept to OPOs, building a comb that spanned 400nm – 2400nm.
Since then we have refined the concept, paying particular attention to understanding the stability available from such OPO combs. We showed that a pump laser with no full comb stabilisation could be used to create a fully stabilized OPO comb, then we measured a stability of around 100 Hz in the optical comb line at 1.5 µm. The linewidth of the individual comb lines is very narrow, since the OPO has no gain storage. The image on the right shows a measurement of a 15-Hz linewidth.
Our current direction of travel is to increase the intermode spacing using Fabry Perot filter cavities, and also to investigate direct routes to higher repetition rates by using direct optical frequency referencig, e.g. to a hyperfine transisition in Rb vapour.
The requirements for the ELT are for comb spacings from 6 GHz (mid-IR) to 30+GHz (uv/visible). We can envisage a combination of OPO and laser routes to address these requirements. Mode flattening filters or even line-by-line shaping should be possible at these repetition rates.

## Slide 4
Motivation – HIRES calibration requirements
Aim to develop novel broadband OPO laser frequency combs for astronomy, such as radial-velocity extrasolar-planet surveys
Core concept is a broadband + tunable OPO
n = "mode order"
f
OPO = optical parametric oscillator
signal
idler
pump
l
femtosecond pump laser
Tunability of a Ti:sapphire pumped PPKTP OPO
Notes: Core expertise in our group is the frequency conversion of modelocked lasers using optical parametric oscillators (“OPOs”) which allow a near-IR laser to be converted into the mid-IR, or (via frequency doubling) into tunable visible light. In 2007 our group was the first to extend the femtosecond frequency comb concept to OPOs, building a comb that spanned 400nm – 2400nm.
Since then we have refined the concept, paying particular attention to understanding the stability available from such OPO combs. We showed that a pump laser with no full comb stabilisation could be used to create a fully stabilized OPO comb, then we measured a stability of around 100 Hz in the optical comb line at 1.5 µm. The linewidth of the individual comb lines is very narrow, since the OPO has no gain storage. The image on the right shows a measurement of a 15-Hz linewidth.
Our current direction of travel is to increase the intermode spacing using Fabry Perot filter cavities, and also to investigate direct routes to higher repetition rates by using direct optical frequency referencig, e.g. to a hyperfine transisition in Rb vapour.
The requirements for the ELT are for comb spacings from 6 GHz (mid-IR) to 30+GHz (uv/visible). We can envisage a combination of OPO and laser routes to address these requirements. Mode flattening filters or even line-by-line shaping should be possible at these repetition rates.

## Slide 5
Doubly-resonant 10-GHz optical parametric oscillator frequency comb
10-GHz Ti:sapphire laser
OPO
SHG
SFM
Rb-ECDL reference
Dither locking
Doubly-resonant 1-GHz optical parametric oscillator frequency comb
1-GHz Ti:sapphire laser
OPO
SHG
SFM
f-to-2f
reference
Dither locking + heterodyne test
Singly-resonant 1-GHz optical parametric oscillator frequency comb
1-GHz Ti:sapphire laser
OPO
SHG
SFM
f-to-2f
reference
Heterodyne locking
OPO comb concepts

## Slide 6
femtosecond laser
An optical parametric oscillator is effectively a "photon splitter"
Every converted pump photon ( ), yields signal ( ) and idler ( ) photons
Wavelength coverage from the visible to the mid-infrared is readily available by adjusting:
  crystal phasematching (in practice, crystal position)
  OPO cavity length (tens of µm adjustment)
Operating Principles
femtosecond OPO
Notes: Heriot Watt has been active in frequency comb research since 2004. We have built a large number of modelocked Ti:sapphire lasers that provided fully-locked combs up to repetition frequencies of 500 MHz. Specifically, we developed a full comb on a single breadboard in 2011 (photo) as a demonstrator for M Squared Lasers, who subsequently licensed the technology from us. This is potentially important in as much as our contribution of comb technology to the ELT project could be supported by M Squared Lasers as potential manufacturing partner.
We have published a number of papers with NPL. In collaboration with Patrick Gill’s group we developed a robust new method for comb stabilisation, which provided a factor of 10 reduction in phase noise compared to the state of the art nonlinear interferometer. The figure below (left) shows graphically the noise improvement we achieved.
In the bottom right figure we show the radio frequency spectrum from our 500-MHz laser, and a zoomed in spectrum of the locked comb offset frequency of 10 MHz. Since 2004 we have increasingly developed more of our own locking electronics, so we have a large amount of control and flexibility in the locking circuits we use.

## Slide 7
Femtosecond laser
f
signal (s)
idler (i)
pump (p)
Synchronously pumped OPOs have near-IR and mid-IR frequency combs with spacing equal to the pump.
Offsets of pump, signal and idler combs described by:
OPO comb offsets are easily tuned by small (nm) changes to the cavity length
Power
  Comb-offset control in a fs OPO
Notes: Heriot Watt has been active in frequency comb research since 2004. We have built a large number of modelocked Ti:sapphire lasers that provided fully-locked combs up to repetition frequencies of 500 MHz. Specifically, we developed a full comb on a single breadboard in 2011 (photo) as a demonstrator for M Squared Lasers, who subsequently licensed the technology from us. This is potentially important in as much as our contribution of comb technology to the ELT project could be supported by M Squared Lasers as potential manufacturing partner.
We have published a number of papers with NPL. In collaboration with Patrick Gill’s group we developed a robust new method for comb stabilisation, which provided a factor of 10 reduction in phase noise compared to the state of the art nonlinear interferometer. The figure below (left) shows graphically the noise improvement we achieved.
In the bottom right figure we show the radio frequency spectrum from our 500-MHz laser, and a zoomed in spectrum of the locked comb offset frequency of 10 MHz. Since 2004 we have increasingly developed more of our own locking electronics, so we have a large amount of control and flexibility in the locking circuits we use.

## Slide 8
sum-frequency-mixing (SFM)
The carrier envelope offset can be measured by using interference between the pump super-continuum and the pump + signal, or pump + idler sum-frequency mixing light e.g. idler CEO:
f
pump super-continuum (s/c)
idler (i)
signal (s)
pump (p)
The beat signal between fS/C and fSFM contains the frequency di, and harmonics of the laser repetition frequency, Frep.
  Principle of detecting the OPO comb offset frequency

## Slide 9
ds locked to 10 MHz with -3-dB linewidth of 15 Hz
Comparable to nominal 10-Hz resolution of the RF spectrum analyzer
Far lower than linewidths of competitive combs:
  Cr:forsterite, 1 MHza
  Er:fibre, 600 kHzb
a Tillman et al, Appl. Opt. 48, 6980 (2009)
b Lim et al, Opt. Express 17, 14115 (2009)
  Experimental detection of the OPO comb-offset signal

## Slide 10
Heterodyne either p+s, 2s or p+i OPO outputs with pump super-continuum
SFM / SHG outputs for a Ti:sapphire-pumped OPO
pS/C
2s
p+s
Heterodyne pS/C : p+i to control the i comb (OPO piezo actuator)  fCEO = fREF
Heterodyne pS/C : 2s to control the p-2s comb  fCEO = fREF
Heterodyne pS/C : p+s to control the s comb  fCEO = fREF
i
p-2s
heterodyne together
  What limits the operating wavelengths of an OPO comb?
s
p+i
degeneracy

## Slide 11
How accurately can the positions of the modes in an OPO comb be controlled?
The frequency of the nth mode fn determined by 2 parameters:
• sub-mHz stability (~10-13), but uncertainty in fn multiplied by n ~ 106
• d sub-Hz level stability (~10-10), contributing only additively to fn uncertainty
 uncertainty in the repetition-rate dominates by factor of ~1000 !
Teresa I. Ferreiro, Jinghua Sun, and Derryck T. Reid, Opt. Express 19, 24159 (2011)
Comb stability characterisations: 250-MHz OPO
fREP
fCEO

## Slide 12
Harmonic pumping, where the OPO cavity is made n times shorter than the pump laser multiplies the repetition frequency by n
Performance compared of 333-MHz and 1-GHz OPO combs, pumped by a 333-MHz Ti:sapphire laser
Comb stability characterisations: 333-MHz & 1-GHz OPOs
K. Balskus, R. A. McCracken, Z. Zhang and D. T. Reid submitted for publication
333 MHz
1.4 W
25 fs

## Slide 13
Harmonic pumping, where the OPO cavity is made n times shorter than the pump laser multiplies the repetition frequency by n
Performance compared of 333-MHz and 1-GHz OPO combs, pumped by a 333-MHz Ti:sapphire laser
Comb stability characterisations: 333-MHz & 1-GHz OPOs
K. Balskus, R. A. McCracken, Z. Zhang and D. T. Reid submitted for publication
333 MHz
1.4 W
25 fs

## Slide 14
Comb offset, d, locked to 10 MHz and measured with 10-Hz resolution bandwidth
Comb stability characterisations: 333-MHz & 1-GHz OPOs
K. Balskus, R. A. McCracken, Z. Zhang and D. T. Reid submitted for publication
333 MHz
1 GHz
Phase-noise power spectral density from 1 Hz – 100 kHz
1.8 rad
2.8 rad
10 Hz @ -3 dB
10 Hz @ -3 dB
27-kHz RIN from pump laser

## Slide 15
Comb stability characterisations: 333-MHz & 1-GHz OPOs
K. Balskus, R. A. McCracken, Z. Zhang and D. T. Reid submitted for publication
1.5 mHz (1s)
0.27 Hz (1s)
333 MHz
0.27Hz (1s)
5 mHz (1s)
1 GHz
ndfREP/fREP
ndfREP/fREP
dfCEO/fCEO
dfCEO/fCEO
dfclock/fclock
dfclock/fclock
fCEO
fCEO
fREP
fREP
Harmonic operation does not compromise the frequency-stability of the comb
Modal stability limited by Rb-quartz reference oscillator to 5 x 10-12 (1-sec gate)

## Slide 16
Towards higher mode spacings:
fundamentally-pumped 1-GHz OPO comb
lsignal 1160 nm 1230 nm 1280 nm 1350 nm
85 fs 87 fs 83 fs 71 fs
Commercial 1-GHz Ti:sapphire pumps OPO directly at 1-GHz mode spacing
Mirror on PZT
silica plate as OC
1 GHz
1.3 W
30 fs
p, i + SFM
CEO interferometer

## Slide 17
Fully stabilized 135-fs OPO frequency comb running at 280 MHz mode spacing
8 x fREP referenced to 2.24-GHz Rb-stabilised microwave synthesiser
Comb offset frequency referenced to a 10-MHz output from the same source.
5x mode filtering (proof-of-principle) in a plano-concave Fabry-Pérot cavity (FSR 1.4 GHz)
OPO frequency comb
l = 1500 nm
Dtp = 135 fs
fREP = 280 MHz
fCEO = 10 MHz
Filtered signal pulses
l = 1500 nm
fREP = 1.4 GHz
Fabry-Pérot filter cavity
PZT1
M1 M2
f = 300 mm
f = 25 mm
PD1
PD2
Towards higher mode spacings:
1.4 GHz OPO comb by Fabry-Pérot filtering
T. I. Ferreiro, T. P. Lamour, J. Sun and D. T. Reid, Electronics Letters 49, 833 (2013)
Frequency (GHz)
1.2 1.4 1.6 1.8 2.0 2.2 2.4 2.6 2.8
-50
-55
-60
-65
-70
Intensity (dBm)

## Slide 18
RF spectrum of the filtered output
Towards higher mode spacings:
Fabry-Pérot filtered 10-GHz OPO comb
RMS length stability of < 0.25 nm
Variance = 0.5%
333 MHz OPO comb (1.35-1.55 μm)
10 GHz comb (1.35-1.55 μm)

## Slide 19
Conclusions
OPO combs
  provide wavelengths which are (at best) marginal from existing laser combs
  can multiply laser mode spacings by harmonic pumping
  can reach 1 GHz and potentially up to 10 GHz directly, without F-P filtering, with potential advantages of lower noise and better sideband suppression
Ongoing research attempting to demonstrate multi-GHz comb operation over an extended wavelength range
Doubly-resonant OPO architecture expected to enable 10-GHz operation
Direct stabilisation to a Rb optical transition will ensure traceability of comb line frequencies, without f-to-2f stabilisation
Applications beyond spectrograph calibration such as dual-comb spectroscopy
Acknowledgements
Dr. Jinghua Sun, Barry Gale, Dr. Teresa Ferreiro, Dr. Richard McCracken,
Dr. Tobi Lamour, Dr. Zhaowei Zhang, Karolis Balskus, Stuart Leitch.
Notes: Core expertise in our group is the frequency conversion of modelocked lasers using optical parametric oscillators (“OPOs”) which allow a near-IR laser to be converted into the mid-IR, or (via frequency doubling) into tunable visible light. In 2007 our group was the first to extend the femtosecond frequency comb concept to OPOs, building a comb that spanned 400nm – 2400nm.
Since then we have refined the concept, paying particular attention to understanding the stability available from such OPO combs. We showed that a pump laser with no full comb stabilisation could be used to create a fully stabilized OPO comb, then we measured a stability of around 100 Hz in the optical comb line at 1.5 µm. The linewidth of the individual comb lines is very narrow, since the OPO has no gain storage. The image on the right shows a measurement of a 15-Hz linewidth.
Our current direction of travel is to increase the intermode spacing using Fabry Perot filter cavities, and also to investigate direct routes to higher repetition rates by using direct optical frequency referencig, e.g. to a hyperfine transisition in Rb vapour.
The requirements for the ELT are for comb spacings from 6 GHz (mid-IR) to 30+GHz (uv/visible). We can envisage a combination of OPO and laser routes to address these requirements. Mode flattening filters or even line-by-line shaping should be possible at these repetition rates.